## Slide 1: Clock Domain Crossing, Why Should I be Concerned?
Dominic Lucido
Technical Account Manager
December 2019
Rick White
Application Engineer Consultant

## Slide 2: Why CDC Verification is a Growing Problem: 10 or More Independent Clock Domains are Common

## Slide 3: 1 in 4 ASIC Re-spins are Caused by Clocking Bugs

## Slide 4: Why CDC is a Growing Problem for FPGA Designers: 4 or More Independent Clock Domains are Common

## Slide 5: Even FPGA Users Are Suffering from Clocking Bugs

## Slide 6: Today’s Design Characteristics
Main Clock Domain
Master IF
Memory
DMA
Master IF
CPU
AMBA AHB/AXI
Master IF
DSP
Arbiter
Slave IF
USB
Controller
USB PHY
Master IF
Ethernet
Ethernet PHY
Master IF
Protocol
PHYs
Bridge
PCI-Express
PCI-E PHY
Slave IF
UART
Bridge
AMBA AHB
Slave IF
GPIO
Slave IF
Custom
Core
Front-end
PHY
Master IF
Custom
Core
Back-end
Power-Management,
Clock, Reset, Test, Analog
Processor cores
DSP cores
Many IP blocks
Sophisticated interconnects
Multiple bus bridges
Advanced power management
Many Asynchronous Clock Domains

## Slide 7: So, What’s The Problem With Clocking Signals?
Logic
A
Logic
Tx
Rx
Clock domain A
Clock domain B
B
Clock-Domain Crossing signal
To transfer signals from one clock domain to another, you need clock-domain crossing (CDC) logic
You CANNOT avoid violating setup and hold timing conditions in this logic

## Slide 8: Why are we here?
If a clock signal is “metastable” the chip can’t run  Re-spin!
1 in 4 FPGA re-spins are caused by CDC Bugs
Multiple clock domains interconnected w/out “synchronizing” will scramble clock signals

## Slide 9: Why do YOU need to worry about CDC?
Re-convergance
Protocol checking
Metastability

## Slide 10: Reconvergence
Invalid Command
CDC signals cross from one domain to another with an assumed relationship
Can be combinational, sequential, or deeply sequential
Unpredictable delays on CDC paths lead to reconvergence errors
  Designs need logic to correctly handle reconvergence
  Can occur on single-bit or multiple-bit signals
S1
S2
S3
S4
FSM Input
tx_d0
tx_d2
tx_d1
Sync 2
Sync 1
Sync 0
0 0 0
0 1 0
0 1 0
0 0 0
0 0 0
0 1 0
Valid Command – but delayed
Grey Encoder
Grey Decoder
0 0 0
1 1 1
1 1 1
0 0 0
1 0 1
1 1 1
Sync 1
0 0 0
0 0 0
1 1 1

## Slide 11: Design for Reconvergence
Apply
Command
To Wrong
Data
ID Comparator ensures that data and command
are aligned prior to processing
Asynch
FIFO
cmd
Asynch
FIFO
data
Apply
Command
to
Data
data
cmd
id
==
valid
id

## Slide 12: Single-Bit Reconvergence
rx_clk
tx_clk
cdc_d
tx_d
rx_q
Metastability delays destroy
correlation between two transitions
rx_clk
cdc_d
rx_clk
rx_q
Notes: In this example, we will look at another type of reconvergence, one that occurs in “time”.
In this example we are transferring a signal between domains. The receiving domain assumes that whenever this signal goes high, it will remain high for a minimum of 2 cycles.
As the signal is transferred, one of the edged (the falling edge) triggers a metastability event due to a setup violation, and the hardware settles to a random zero. This means that the hardware has advanced the edge (relative to simulation) by one cycle.
The end result is that in the receiving domain the signal is now no longer high for the duration expected and the relationship between the edges has been destroyed leading to a potential problem.
Both of these types of reconvergence problems “space” and “time” can be fixed through good design.

## Slide 13: CDC Transfer Protocols
Synchronization structures require a transfer protocol
  Ensures data is predictably transferred between domains
These protocols must be verified
When protocol is violated
  Data is lost or corrupted
  Metastability may occur
  Simulation may not show a failure
  Silicon will eventually show a functional error

## Slide 14: Metastability Is Not Detected by RTL Simulation
Image source: http://www.fpga-faq.com/Images/meta_pic_1.jpg
Simulation captures a ‘1’ while silicon produces either a ‘1’ or ‘0’
Simulation captures a ‘0’ while silicon produces either a ‘1’ or ‘0’
CDC signals are subject to metastability when timing violations occur

## Slide 15: CDC Paths Cause Metastability
When a CDC signal changes values between the setup or hold time of a receiving domain’s register
Receiving register becomes metastable
  Settles to a random value, after unknown amount of time
Happens even with proper synchronization & protocols
Can cause significant functional problems in the design
Clock
D
Hardware Q
Data Sampled
Notes: 15

## Slide 16: Metastability Happens
Every type of storage element is susceptible to metastability
  It’s just a matter of time…
Can your design handle it?
fclk = Clock Frequency
fin = Input Signal Frequency
td = Duration of critical time window
Notes: 16

## Slide 17: Manual ways to mitigate the effects of CDC
Using synchronizers
Ad-hoc coding styles to circumvent crossings

## Slide 18: CDC Synchronizers
Designers add synchronizers to reduce the probability of metastable signals
Synchronizers are sub-circuits that prevent metastable values from being sampled across clock domains
  Take unpredictable metastable signals and create predictable behavior

## Slide 19: CDC Synchronizers (continued)
Many different synchronizer types
  “Structured” and “Ad hoc”
Each synchronizer follows strict rules for that must be verified
But…
  Synchronizers can only resolve unpredictable values
  Synchronizers cannot resolve unpredictable delays
Glitch
Free
Output
Single
Point
Sampling
Full
Cycle
To Settle

## Slide 20: Ad-Hoc methods
For multibit signals such as buses, the usual solution is to use a Gray code when crossing a clock domain boundary. A Gray code ensures that only a single bit changes as the bus counts up or down. This makes it possible to detect whether all bits have been captured together by the receiving clock or if they have been skewed across multiple clock cycles due to metastability or differing delays among the bus bits.
For example, in an asynchronous FIFO, the read and write pointers cross over to the write and read clock domains, respectively. These pointers are control signals that are flop-synchronized. The signals are Gray-encoded prior to the crossover.

## Slide 21: Using automated solutions (Questa CDC) to uncover issues
Automated checking for proper use of Synchronizers
Automated checking of re-convergence
Seeing the effects of clocks when they go metastable

## Slide 22: Questa Formal Solutions & Apps Automated, Exhaustive Verification For Complex Challenges

## Slide 23: Questa Formal-Based Solutions & Apps Automated, Exhaustive Verification For Each Project Phase

## Slide 24: What’s Driving Customer Adoption of Questa CDC?
Highest performance & scalability
Automated, thorough, hierarchical approach
Contextual guidance to leverage over 50 CDC schemes
Dynamic CDC analysis integrated with QuestaSim
UCDB from Questa CDC can be sent to Questa Verification Management to track progress over multiple runs

## Slide 25: Questa CDC Advantages
Accuracy
Scalability
Guidance

## Slide 26: Questa CDC for FPGA Users
CDC bugs look like STA  CDC saves weeks of lab time!
MGC advantages: QoR, debug, corrective guidance
New Xilinx Vivado integration simplifies setup & run
Supported devices:

## Slide 27: Enhancing the Questa CDC + FPGA Workflow
Simplifying the end-users’ job
Creating a GUI-centric flow that FPGA users prefer
Importing the project file of FPGA Vendor to expedite setup
Automatically streamline analysis for FPGA-specific architecture & primitives
UCDB
Waivers,
Constraints
Questa
CDC
GUI-based work flow & reports
“CDC-FX” Metastability
models
for functional simulation
RTL
SDC
Recommended
Synchronizers

## Slide 28: Questa CDC ASIC Workflow
UCDB
Waivers,
Constraints
Questa
CDC
Textual & GUI Reporting
“CDC-FX” Metastability
models
for functional simulation
RTL
SDC
UPF
Recommended
Synchronizers

## Slide 29: Wide Spectrum of Synchronizers for Solving Any CDC Issues
2DFF
DMUX
Handshake
FIFO
Asynchronous reset
… and more built-in …
< Customize your own >

## Slide 30: Hierarchical CDC Analysis
Enables analysis of larger designs
  Divide and conquer
  Reduce memory footprint
Enables abstraction of block-level representation
  Netlist model (gray box)
  Interface only model (black box)
Enables parallel verification of multiple blocks
  Reduce total time to verify the entire design
Safer, thorough approach that can find more bugs
Top
Block
Level
CDC
Top
Top-level setups
Propagate top-level setups
Top-level checks
Integrated results
Block
Level
CDC
Block
Level
CDC
Block
Level
CDC
Block
Level
CDC
Top-down flow
Bottom-up flow

## Slide 31: CDC Enhanced Reporting and Debugging
Provides a results overview window and details for all CDC issues
Automatically generates schematics for visualization of clock trees and CDC paths

## Slide 32: Questa CDC Generates Automatic Protocol Checks
CDC protocols defined
  Rules that ensure data is accurately transferred between two clock domains
  Associated with specific synchronizer structures
The Questa CDC verification solution automatically generates assertions to capture these protocols
Seamless integration / transfer of generated assertions into Questa Formal or QuestaSim
Formal & simulation results are automatically correlated back to the source synchronizer for easy debug
Assertion
Protocol Example: When a transmitter's data select signal crosses a clock domain and drives the mux select input (a) of a data multiplexer in the receiver, it must be held stable long enough for the signal (b, TX Data) to be sampled reliably by the receiver (c, RX Data) and the data must remain stable while the data select signal asserts.
(a) Mux select
(b) TX Data
(c) RX Data

## Slide 33: Questa CDC Protocol Assertion Flow
CDC Protocol Assertions
RTL
Proven Assertions
RTL
Formally prove CDC protocols are implemented correctly – fully automatic
Simulate CDC protocol assertions jointly with the design and testbench
CDC Protocol Assertions
Simulation
Non-proven
Covered Assertions
Coverage Reporting
RTL &
Testbench
Review Assertion Violations
Questa CDC
Static Analysis
Questa Formal Analysis

## Slide 34: Questa CDC Protocol Verification Details
Automatic SVA protocol checker generation
  Synchronizer-specific protocol assertion macros instantiated
  Protocol checkers include assertions and coverage
Simulation generates CDC database
  Assertion and coverage data captured during simulation
Formal CDC verification
  Exhaustive protocol verification results through formal analysis
  Automated formal verification setup
Integrated protocol results viewing
  View protocol assertion and coverage results
  Correlate protocol results with structural CDC results
Enables protocol verification closure
  Coverage measures protocol verification progress and completeness
  Identify and fix coverage holes

## Slide 35: Questa CDC Driving Formal or Simulation-Based Protocol Verification
All CDC protocol violations are shown in CDC analysis window
Debug is performed in formal or simulation environment
Highlights exactly where a protocol violation occurs

## Slide 36: Dynamic CDC Analysis for Verifying Resiliency
Tx
Rx
clk_A
D
Q
D
Q
D
Q
2DFF Synchronizer
Metastability Checker
Driver
Behavioral Metastability Model (BMM)
clk_B
i
i +1
i +2
i -1
i +3
Setup violation
Tx
clk_B
Rx
Rx
Simulation with “Behavioral Metastability Models” is the ONLY way to verify whether the design is resilient w.r.t. non-deterministic delays in synchronizers
Questa “CDC-FX” generates the models
Include metastability models in simulation to access impact of synchronizer choice

## Slide 37: CDC Errors are Painful!
Usually not caught by simulation
Found late in the development cycle
  Often only in silicon
Silicon failures are intermittent
  Difficult to reproduce
  Difficult to debug
Lot’s to consider:
  Re-convergance
  Protocol checking
  Metastability

## Slide 38: Questa CDC Summary The industry benchmark for CDC verification
All designs with multiple, asynchronous clock domains require a CDC verification solution to avoid costly bugs
Questa CDC offers:
  The industry’s leading clock-domain crossing verification solution
  Complete and accurate CDC reporting, protocol verification, and metastability modeling
  A proven track record and an exacting hierarchical approach
Includes support for power-aware CDC analysis and functional simulation